## Slide 1
XrootD Third-Party Transfers Using dCache
Albert Rossi
Dmitry Litvintsev
Fermi National Accelerator Laboratory

## Slide 2
How it works
User client contacts source and destination servers to see if TPC is supported
User client generates rendezvous token, or uses delegation
Servers communicate using the token, or with delegated proxy
Destination pulls (reads) from source using server-side client (in XrootD, this is an xrdcp process; in dCache, the client is embedded)

## Slide 3
Source
Destination
(TPC client)
How it works (protocol specification)
stat (file should not exist)
open/close (file should exist)
open (w/ rendezvous metadata)
sync (starts tpc client)
open (w/ rendezvous metadata or delegation)
read (pull) and write locally ...
sync (blocks until tpc client close)
close
sync (reply)
open (w/ rendezvous metadata)
close
close
...
(asynchronous wrt open from tpc client [and skipped if credential delegation is used])
?

## Slide 4
Source
Destination
(TPC client)
stat (file should not exist)
open/close (file should exist)
open (w/ rendezvous metadata)
sync (starts tpc client)
open (w/ rendezvous metadata or delegation)
read (pull) and write locally ...
sync (blocks until tpc client close)
close
sync (reply)
close
close
...
(asynchronous wrt open from tpc client [and skipped if credential delegation is used])
?
redirect to pool
open (w/ rendezvous metadata)
start mover
start mover
open (w/ rendezvous metadata)
Door
Pool
Pool
Door
(read mover is started when both client and destination have called open [no delegation], or when destination opens)
How it is implemented in dCache
redirect to pool
open

## Slide 5
TPC Authentication with dCache
Unauthenticated
GSI (x509 certificate-based)
dCache provides three options for (2)
    Use proxy automatically generated from host certificate (on pools) [dCache 4.2+]
    Use externally generated proxy (on pools) [dCache 4.2+]
    Full proxy delegation [dCache 5.2+]

## Slide 6
TPC Authentication with dCache
    (1) proxy automatically generated from certificate (e.g., host)
    - requires cert and key .pem on all affected pool nodes
    - refreshed/regenerated by dCache
    - pre-5.1: need to map all pool DNs (on all potential source endpoints!)
    (2) externally generated proxy
    - required on all affected pool nodes (indicated by path)
    - requires external cron to refresh
    (3) full proxy delegation
    - no extra configuration necessary
    dCache 5.2 defaults to (3) if delegation is requested/supported by the client; otherwise it will try (1) unless the path for (2) is configured.
    Note that dCache 5.1+ allows for anonymous (authenticated) fallback during the server-to-server communication, so gPlazma mapping of the destination DN is not necessary in the case of 1 or 2 (it just needs to come from a recognized CA). Turn this on via property (see later slide).

## Slide 7
Authentication with Security Level
    XrootD security level
    added protection against man-in-the-middle attack
    requests preceded by signed hash which must be verified
    from minimal (level 1) to maximal (level 4), where 4 means all requests sent after the authentication handshake completes
    not just for third-party-copy
    dCache 5.0+ implements security/signed hash verfication for both the door (server) as well as in the TPC client.
    dCache “gotcha”: see next slide

## Slide 8
client
client
GSI
No Authn
GSI
Unix
dCache UUID
Pools: No Authn vs. Unix Authn
Level = 0 (off)
Level > 0 (on)
dCache UUID
dCache UUID
dCache UUID
dCache UUID
dCache UUID

## Slide 9
Authentication with Security Level
    To turn signed hash verification on, there must be an authentication protocol active (xrootd cannot sign hashes with no authn).
    dCache has traditionally not required re-authentication on redirect to the pool, since it generates a UUID token for the client to use during the transfer.
    In order to support security level on the pools, the pools require the “placeholder” minimal protocol (unix), so that xrootd endpoints will honor the request for signed hash verification.
    The unix protocol, however, is unencrypted; an extra flag must be set to force sending unencrypted hashes.
    In dCache, it currently does not make much sense not to use this option, because after open, most of the activity (sync, stat, read, write, close, etc.) is on the pool.
    Question as to usefulness; whether we need GSI on the pools as well? An unwarranted burden? ...

## Slide 10
Enabling TPC (XrootD client)
    xrdcp 4.8+
    to enforce third-party copy:
    xrdcp --tpc only root://<source> root://<destination>
    to try third-party copy but fail over to 1-hop:
    xrdcp --tpc first root://<source> root://<destination>
    xrdcp 4.9+
    to delegate the proxy:
    xrdcp --tpc delegate only root://<source> root://<destination>
    xrdcp --tpc delegate first root://<source> root://<destination>

## Slide 11
XrootD TPC in dCache – version requirements
    To use dCache as the source in XrootD TPC
        update to version 4.2+ on the nodes running the xrootd doors
    To use dCache as the destination in XrootD TPC
    update to version 4.2+ on the nodes running the xrootd doors and all relevant pools
    To enable security level support
    update to version 5.0+ on the nodes running the xrootd doors and pools
    To enable anonymous authenticated reads by TPC destination client
    update to version 5.1+ on the nodes running the xrootd doors
    To enable full GSI proxy credential delegation
    update to version 5.2+ on the nodes running the xrootd doors and pools

## Slide 12
Version Compatibility
    SLAC/XrootD servers and clients for 4.9+ are backward compatible with 4.8+, meaning they can tell (from the protocol version communicated during handshake) whether or not to (try to) use proxy delegation.
    Also true for dCache 5.2. Can be used for TPC with dCache 4.2+ and SLAC/XrootD 4.8+ (client and server), and will be able to determine whether delegation is supported or not.
    Of course, if delegation is not supported, then dCache needs to be configured to fail over correctly. This involves making a credential available on the pools, and DN recognition.

## Slide 13
Configuring GSI for TPC -- Doors
    as usual, enable GSI on the doors via:
    xrootd.plugins=gplazma:gsi,...
    dCache as source requires gPlazma to recognize as valid the credential of the destination (client)
          v5.1+ – to allow the destination client read-only access (even to read-protected files), set:
          xrootd.plugins=gplazma:gsi,authz:none
            xrootd.authz.anonymous-operations=READONLY
            otherwise, mapping needs to be done for all potential client endpoints when delegation is not used.

## Slide 14
Configuring GSI for TPC -- Pools
    dCache as destination requires a pool plugin to be set:
    pool.mover.xrootd.tpc-authn-plugins=gsi
          a pool-side credential must be available for the third-party client to use
            option 1: proxy auto-generated from .pem files; these default to location for hostcert
            and hostkey, but can be overridden via properties beginning with:
            xrootd.gsi.tpc.cred...
            option 2: use externally generated and refreshed proxy; path indicated by:
            xrootd.gsi.tpc.proxy.path
            option 3: full proxy delegation (no further configuration necessary)

## Slide 15
Configuring GSI for TPC -- Pools
    to support pre-4.9 xrdcp clients wishing to do TPC using dCache as destination, the pools must be configured using one of the first two options; in the case of delegating clients, the pool-side credential will be ignored in favor of the delegated proxy.
    all relevant properties for GSI are found in:
    xrootd-gsi.properties

## Slide 16
Configuring Security Level (5.0+)
    The embedded third-party client will honor signed hash verification if the source server indicates it must be observed.
    5.0+ provides the following properties to set server/door security level:
    dcache.xrootd.security.level={0-4}
    dcache.xrootd.security.force-signing={true,false}
    In order to enforce a security level > 0 on the pools, the second property must be set to true
    If one anticipates there will be TPC transfers between two dCache instances or two dCache doors, the ‘unix’ plugin must be added to all the relevant pool configurations:
    pool.mover.xrootd.tpc-authn-plugins=gsi,unix
    See further the xrootd.properties file.

## Slide 17
Troubleshooting
    The xrdcp client allows for –d 1-3 debugging output. This can be useful for some things, but unfortunately is more verbose than diagnostically revealing for things like authentication issues.
    For connection and authentication issues, check first the .access logs for both the doors and pools.
    The pinboard running at INFO level can sometimes reveal the issue: e.g.,

## Slide 18
Troubleshooting
    A rather extensive output can be activated at the debug-level:
    \s <door>,<pool>,... log set stdout org.dcache.xrootd DEBUG
    In addition, byte dumps of the authentication handshake can be printed by turning on trace-level debugging. This may be useful to send to the developers (me) in case of an unusual authentication failure. The byte dumps are printed to resemble those produced by the SLAC xrootd implementation.
    \s <door>,<pool>,... log set stdout org.dcache.xrootd TRACE

## Slide 19
Possible Future Work
    Optimize door-to-door (dCache to dCache) TPC not to use the rendezvous token (similarly to the XrootD server)
    Support SciTokens
    Enable vector reads in the third-party-client

## Slide 20
    A special note of thanks goes to the SLAC xrootd development team for their helpful responses and collaborative spirit, in particular, Andy Hanushevsky, Wei Yang, Michal Simon and Gerri Ganis.